Getting started:

1)Installation
>git clone https://github.com/wdklotz/simulinac XXX
Use the command above to clone the latest version into the directory XXX.

2)run the sample
Make shure you use pyhton 3
cd to XXX
>python simu.py [<input-file>]

3) If it works - bingo!

4)Input (*.yml)
Default sample input-file is „XXX/yml/25_09_2017_versuche_70_200MeV.yml“.
This input file is loaded with lots of comments which explain how to set up input for simu.py.
Be aware: its syntax is YAML which is very picky with indentation!
Edit filepath at the end of simu.py if you want other default input files.

5)Features of simu.py can be controlled by following definitions:

5.1)flags:
Most of them are commented. If so, they are set to their default values which are shown in brackets {....}. If you want to activate uncomment! Most important are:
sigma: if True beam size is calculated from sigma matrix formalism else from twiss	functions.
express: if True quadrupoles are replaced by fast implementations of thin-lense	matrices else the thin-lens is calculated as triplet product D*KICK*D.

5.2)sections:
Two sections are defined in the sample LE and HE like
- [&<section alias><space><name>,&<section alias><space><name>,….]
Only HE is used in the sample.

5.3)parameters:
Physics and lattice parameter definitions like:
- <name>: &<parameter alias><space><value> | <value> | *<parameter alias>
Some parameter names (see the sample input) are recognized by the program and used as starting conditions. They are: aperture, betax_i, alfax_i, emitx_i, betay_i, alfay_i, emity_i, sigmaz_i, dp2p_i, frequency and Tkin. Others are of free choice to be used in element definitions.

5.4)elements:
Definition of elements
1st line	- <ID>: &<element alias>	#any ID you like
2nd line	- type: <CLASS>	#defines the lattice element
attribute 1	- <key>: *<parameter alias> | <value>
:
attribute N	- <key>: *<parameter alias> | <value>
All attribute keys with exception sec: *<section alias> are mandatory and depend on the element CLASS.

5.4.1)Element CLASS definitions:
I	NOP unit
D	Drift
SIXD	Drift with SixTrack mapping
QF	thick F quadrupole with slices option
QD	thick D quadrupole with slices option
RFG	RF gap with mapping options (ref. T3D and A.Shishlo)
RFC	RF cavity as triple product D*RFG*D
GAP	Simple zero length RF-gap w/o (s,dp/p) (ref. Dr.Tiede & T.Wrangler)
M	Marker with action attributes
SD	T3D sector dipole in x-plane
RD	T3D rectangular dipole x-plane
WD	T3D dipole wedge x-plane
QFth	thin F quadrupole
        QDth	thin D quadrupole
QFthx	thin express F quadrupole
        QDthx	thin express D quadrupole

5.4.2)CLASS „RFG“ has a mapping attribute which can be one of „t3d“, „simple“, „base“, „ttf“ or „dyn“. „base“ is a simplified non-linear map assuming constant time-transition factors. „simple“ is pyOrbit‘s linear map. „t3d“ uses TRACE 3-D matrix maps and gives same results as „simple“. „ttf“ uses pyOrbit‘s 3 point Transit Time Factors RF gap-model using Ez(r=0) field data calculated with SuperFish. „dyn“ uses the DYNAC gap-model focused on a numericla step-by-step method based on the 5-points Bode‘s rule with Picht coordiante transformations. It uses the same externaly provided SuperFish data.

5.4.3)CLASS „RFG“ has also the SFdata attribute which has to be set to the name of the file containing the field profile data from SuperFish.

5.4.4)CLASS „QF“ and „QD“ have a slices attribute which can take values [1,…,N]. if N=1 the thick T3D matrix is used elif N>1 the quadrupole is cut into N slices of thin-lens quadrupoles, either as D*KICK*D or „express“.

5.4.5)CLASS „SIXD“ is a symplectic drift space mapping using SixTrack canonical coordinates. Slows the calculation sensibly down and is useful to check final results.

5.4.6)CLASS RFC uses RFG with „t3d“ mapping as zero length cavity kick.

6)segments:
A segment is defined as:
- <seg name>:	#any name you like
- *<element alias>
- *<element alias>
        :
7)lattice:
Finally the lattice is defined as
1st line	- title: <any text> # must be present as 1st line!
lines below	- [N, <seg name>,<seg name>,…,<seg name>]
lines below	- [N, <seg name>,<seg name>,…,<seg name>]
      :
Number N expands the segment list in same brackets N times. Many segment lines can be given, for instance one for each section.